## Slide 1: Power Transmission Case Study
Max Van Huis, Lillian Wilson, Andrew Vitale
April 30, 2025
Machine Component Design MAE 353 01

## Slide 2: Background
We were interested in creating a gearbox that can convert a higher rpm input to a higher torque output.
Main steps were as follows:
  Gear design
  Shaft design and selection
  Bearing selection

## Slide 3: Background (continued)
Gear reducers can be found in high-torque machines
Examples include:
  Agricultural machinery
  Trucks
  Construction machinery

## Slide 4: Drawings

## Slide 5: Detailed Design: Power and Torque Req.
Given Power: 17 HP
Input Speed: 1600 rpm
Output Speed: 80-85 rpm
Bearing Life: 14,000 hours

## Slide 6: Detailed Design: Gear Specs and Forces

## Slide 7: Detailed Design: Shaft Specs and Forces
Shaft | Torque | 
1 | 669.6406 | lb*in.
2 | 2976.181 | lb*in.
3 | 13227.47 | lb*in.
Resultant Forces at Gear Locations (Y direction) |  |  | 
Pinion 1 | -212.0213 | lbf | 
Gear 2 | 308.0698 | lbf | 
Pinion 3 | 967.5146 | lbf | 
Gear 4 | -871.4661 | lbf | 
Resultant Forces at Gear Locations (X direction) |  |  | 
Pinion 1 | -595.2395 | lbf | 
Gear 2 | 595.2395 | lbf | 
Pinion 3 | -2645.509 | lbf | 
Gear 4 | 2645.509 | lbf | 

## Slide 8: Detailed Design: Shaft Bending Moments

## Slide 9: Detailed Design: Bearing Specs and Forces
Required Bearing Capacities |  |  | 
 | NEW | OLD | 
Creq (B1) | 3.64 | 3.57 | kN
Creq (B2) | 3.97 | 4.04 | kN
Creq (B3) | 3.19 | 3.12 | kN
Creq (B4) | 15.87 | 15.95 | kN
Creq (B5) | 7.20 | 7.33 | kN
Creq (B6) | 6.62 | 6.49 | kN
 | Less | More | 

## Slide 10: Recommendations
Lower the diameter on the stepped shaft.
  Use helical gears and herringbone gears
    Helical gears engage more gradually than spur gears
    Herringbone gears eliminate the axial thrust generated by the gears.
  Use a stronger materials such as AISI 4130
    Contains chromium and molybdenum as strengthening agents

## Slide 11: Conclusions
We learned how tedious each step and system of the design was.
  One small edit changes the entire design
Continued to develop skills on excel and using CAD software.
  Excel was great for design selection changes.

## Slide 12: References
Khkgears.net, 2025, khkgears.net/new/images/know-about-parameters-that-determine-gear-shapes/Parameters- necessary-for-gear-design.jpg. Accessed 29 Apr. 2025.
Skyhighelearn.com, 2021, skyhighelearn.com/wp-content/uploads/2021/03/Design-of-procedure.jpg. Accessed 29 Apr. 2025.
Principle-Eng.co.uk, 2025, principle-eng.co.uk/wp-content/uploads/2016/12/GRW-Ball-Bearings-Deep- Groove-470x470.jpg. Accessed 29 Apr. 2025.
Orleanshub.com, 2023, orleanshub.com/wp-content/uploads/2023/07/072223_Mhaywire.jpg. Accessed 29 Apr. 2025.
Picture Credit:
Juvinall, Robert C, and Kurt M Marshek. Fundamentals of Machine Component Design. Hoboken, N, Wiley, 2020.

## Slide 13: Questions?